## Slide 1: Topology
It is the shape or physical connectivity of the network.
Goals when establishing topology
  Provide maximum possible reliability to assure proper receipt of all traffic
  Route the traffic across the least cost path within the network.
  Give the end user the best possible response time and throughput
Each topology has advantages & disadvantages

## Slide 2: Types of Topologies
Star
  Easy to install
  Central element, a hub or a switch
  Localisation of problem
  Hub is the weakest element
Bus
  Easy to expand, shorter cables
  Single conversation, all station can hear every transmission
  Bus is the weakest element

## Slide 3: Types of Topologies
Ring
  Deterministic
  Dual path, redundant
  Poor scalability
Line
  Open ring
Tree
  Mesh network with no redundancy
  Provides a concentration point for control and error resolution and potential bottleneck

## Slide 4: Types of Topologies
Mesh
  Multiple paths are available
  Reconfiguration possible
  Multiple hops
  Wiring complicated
Fully connected network
  Extended mesh network
  Fast, no hops
  Poor scalability
30

## Slide 5: Ethernet
Outline
Multiple Access and Ethernet Intro
Ethernet Framing
CSMA/CD protocol
Exponential backoff

## Slide 6: Multiple Access Methods
Fixed assignment
  Partition channel so each node gets a slice of the bandwidth
  Essentially circuit switching – thus inefficient
  Examples: TDMA, FDMA, CDMA (all used in wireless/cellular environments)
Contention-based
  Nodes contends equally for bandwidth and recover from collisions
  Examples: Aloha, Ethernet
Token-based or reservation-based
  Take turns using the channel
  Examples: Token ring

## Slide 7: Our Focus is Ethernet
History
  Developed by Bob Metcalfe and others at Xerox PARC in mid-1970s
  Roots in Aloha packet-radio network
  Standardized by Xerox, DEC, and Intel in 1978
  LAN standards define MAC and physical layer connectivity
    IEEE 802.3 (CSMA/CD - Ethernet) standard – originally 2Mbps
    IEEE 802.3u standard for 100Mbps Ethernet
    IEEE 802.3z standard for 1,000Mbps Ethernet
CSMA/CD: Ethernet’s Media Access Control (MAC) policy
  CS = carrier sense
    Send only if medium is idle
  MA = multiple access
  CD = collision detection
    Stop sending immediately if collision is detected

## Slide 8: Ethernet Standard Defines Physical Layer
802.3 standard defines both MAC and physical layer details
Metcalfe’s original
Ethernet Sketch

## Slide 9: Ethernet Technologies: 10Base2
10: 10Mbps; 2: under 185 (~200) meters cable length
Thin coaxial cable in a bus topology
Repeaters used to connect multiple segments
  Repeater repeats bits it hears on one interface to its other interfaces: physical layer device only!

## Slide 10: 10BaseT and 100BaseT
10/100 Mbps rate
T stands for Twisted Pair
Hub(s) connected by twisted pair facilitate “star topology”
  Distance of any node to hub must be < 100M

## Slide 11: Physical Layer Configurations for 802.3
Physical layer configurations are specified in three parts
Data rate (10, 100, 1,000)
  10, 100, 1,000Mbps
Signaling method (base, broad)
  Baseband
    Digital signaling
  Broadband
    Analog signaling
Cabling (2, 5, T, F, S, L)
  5 - Thick coax (original Ethernet cabling)
  F – Optical fiber
  S – Short wave laser over multimode fiber
  L – Long wave laser over single mode fiber

## Slide 12: Ethernet Overview
Most popular packet-switched LAN technology
Bandwidths: 10Mbps, 100Mbps, 1Gbps
Max bus length: 2500m
  500m segments with 4 repeaters
Bus and Star topologies are used to connect hosts
  Hosts attach to network via Ethernet transceiver or hub or switch
    Detects line state and sends/receives signals
  Hubs are used to facilitate shared connections
  All hosts on an Ethernet are competing for access to the medium
    Switches break this model
Problem: Distributed algorithm that provides fair access

## Slide 13: Ethernet Overview (contd.)
Ethernet by definition is a broadcast protocol
  Any signal can be received by all hosts
  Switching enables individual hosts to communicate
Network layer packets are transmitted over an Ethernet by encapsulating
Frame Format
Dest
addr
64
48
32
CRC
Preamble
Src
addr
Type
Body
16
48

## Slide 14: Switched Ethernet
Switches forward and filter frames based on LAN addresses
  It’s not a bus or a router (although simple forwarding tables are maintained)
Very scalable
  Options for many interfaces
  Full duplex operation (send/receive frames simultaneously)
Connect two or more “segments” by copying data frames between them
  Switches only copy data when needed
    key difference from repeaters
Higher link bandwidth
  Collisions are completely avoided
Much greater aggregate bandwidth
  Separate segments can send at once

## Slide 15: Ethernet Frames
Preamble is a sequence of 7 bytes, each set to “10101010”
  Used to synchronize receiver before actual data is sent
Addresses
  unique, 48-bit unicast address assigned to each adapter
    example: 8:0:e4:b1:2
    Each manufacturer gets their own address range
  broadcast: all 1s
  multicast: first bit is 1
Type field is a demultiplexing key used to determine which higher level protocol the frame should be delivered to
Body can contain up to 1500 bytes of data

## Slide 16: Ethernet’s MAC Algorithm
In Aloha, decisions to transmit are made without paying attention to what other nodes might be doing
Ethernet uses CSMA/CD – listens to line before/during sending
If line is idle (no carrier sensed)
  send packet immediately
  upper bound message size of 1500 bytes
  must wait 9.6us between back-to-back frames
If line is busy (carrier sensed)
  wait until idle and transmit packet immediately
    called 1-persistent sending
If collision detected
  Stop sending and jam signal
  Try again later

## Slide 17: State Diagram for CSMA/CD
Packet?
Sense Carrier
Discard Packet
Send
Detect Collision
Jam channel b=CalcBackoff(); wait(b);
attempts++;
No
Yes
attempts < 16
attempts == 16

## Slide 18: Collisions
A
B
A
B
Collisions are caused when two adaptors transmit at the same
time (adaptors sense collision based on voltage differences)
  Both found line to be idle
  Both had been waiting to for a busy line to become idle
A starts at
time 0
Message almost
there at time T when
B starts – collision!

## Slide 19: Exponential Backoff
If a collision is detected, delay and try again
Delay time is selected using binary exponential backoff
  1st time: choose K from {0,1} then delay = K * 51.2us
  2nd time: choose K from {0,1,2,3} then delay = K * 51.2us
  nth time: delay = K x 51.2us, for K=0..2n – 1
    Note max value for k = 1023
  give up after several tries (usually 16)
    Report transmit error to host
If delay were not random, then there is a chance that sources would retransmit in lock step
Why not just choose from small set for K
  This works fine for a small number of hosts
  Large number of nodes would result in more collisions