## Slide 1
Connecting to an existing Wi-Fi network
Setting up Node MCU as an Wi-Fi Access Point
Create a HTTP Server hosted by Node MCU
DNS masking of IP assigned by the AP
Controlling GPIO Through REST APIs
Reading ADC Value through REST APIs
HTTP REST Server - Node MCU
Objectives : -

## Slide 2: Connecting to an existing Wi-Fi network
#include <ESP8266WiFi.h>
  Header File
WiFi.begin(<ssid>,<password>);
  Setting SSID and Password of the AP
while (WiFi.status() != WL_CONNECTED)
  Check Wi-Fi status
WiFi.localIP()
  Read IP Address Assigned

## Slide 3: Setting up Node MCU as an Wi-Fi Access Point
include<ESP8266WebServer.h>
  Header File
ESP8266WebServer server;
  Web server variable
server.on("/", []() { server.send(200,"text/plain", "Hello World.. ! "); });
  Home Page of the server
server.on("/<path>", <callback Function>);
  Setting up a function that will be executed if the <path> is called
server.handleClient();
  Default method to handle the clients

## Slide 4: Create a HTTP Server hosted by Node MCU
#include <ESP8266WiFi.h>
  Header File
IPAddress ip(192, 168, 11, 4);
  Setting up IP for setting up as an AP
IPAddress gateway(192, 168, 11, 1);
  Setting up Gateway for setting up as an AP
IPAddress Subnet(255,255,255,0)
  Setting up Subnet for setting up as an AP
WiFi.softAPConfig(ip, gateway, subnet);
  Applying options for AP
WiFi.softAP(<SSID>,<Password>)
  Starting the Wifi AP

## Slide 5: DNS masking of IP assigned by the AP
#include <ESP8266mDNS.h>
  Header File
MDNSResponder mdns;
  Dns Responder variable
MDNS.addService("http", "tcp", 80);
  Adding the server

## Slide 6: Controlling GPIO Through REST APIs
server.on("/toggle", toggleLED);
  Go to <ip>/toggle and it call toggleLED Function
void toggleLED() { flag = 0; digitalWrite(pin_led, !digitalRead(pin_led)); server.send(200, "text/plain", "LED Toggled!"); }
  Callback function of /toggle
  Toggling the LED
  Displaying LED Toggled on the Web Page

## Slide 7: Reading ADC Through REST APIs
client.print("analog input ");
client.print(<ANALOG_PIN>);
client.print(" is ");
client.print(sensorReading);
client.println("<br />");
  Reading analog data
  Creating String to be displayed as a web page
  Go to <ip>/to get adv value
pinmode(24,INPUT)//analog pin of esp32--set in void setup

## Slide 8: Thank You
Follow the link for sample code : -
https://github.com/ersanyamarya/Node-Mcu-HTTP-REST-Server