## Slide 1: Programming NodeMCU/ESP32 using Arduino IDE

## Slide 2: PART1
NodeMCU (ESP8266)

## Slide 3: NodeMCU (LoLin)
Open source hardware.
Anyone can produce and market NoduMCU development board.
There are three primary producers.
  Amica
  DOIT/SmartArduino
  Lolin
ESP-12E Module.
CH340G USB to serial converter.
ASM1117 Voltage regulator.

## Slide 4: ESP-12E
Wi-Fi 2.4 GHz, support WPA/WPA2
802.11 b/g/n
Integrated low power 32-bit MCU - Tensilica L106
  - 80MHz
  - VDD - 3.3V
  - Integrated 10-bit ADC
  - SPI, UART, I2C, PWM, GPIO
Notes: Note: The ESP8266 is a low-cost Wi-Fi chip with full TCP/IP stack and MCU (Micro Controller Unit) capability produced by Shanghai-based Chinese manufacturer, Espressif Systems. They design the chip and other OEMs manufacture it.
ESP-12E is made by a third-party manufacturer, AI-Thinker. Documentation for it is sparse.

## Slide 5: CH340G (USB to Serial chip)
Full-speed USB device that emulates a standard serial interface.
Used for flashing your code to ESP-12E & serial communication.
Baud rate 115200.
Notes: Note: NodeMCU can be used with the help of
- Espressif SDK.
- NodeMCU Lua firmware.
- Arduino IDE (using Arduino core).
Espressif SDK:
The ESP8266 was designed and is fabricated in China by Espressif Systems. Espressif have also developed and released a companion software development kit (SDK) to enable developers to build practical IoT applications for the ESP8266. The SDK is made freely available to developers in the form of binary libraries and SDK documentation. However this is in a closed format, with no developer access to the source files, so ESP8266 applications must rely solely on the SDK API.
NodeMCU firmware:
The NodeMCU firmware implements Lua 5.1 over the Espressif SDK for its ESP8266 SoC.
The NodeMCU Lua firmware is an ESP8266 application and must therefore be layered over the ESP8266 SDK.
The firmware has replaced some standard Lua modules that don't align well with the SDK structure with ESP8266-specific versions (standard io & os libraries don’t work).
NodeMCU Lua is based on eLua, a fully featured implementation of Lua 5.1 that has been optimized for embedded system development and execution to provide a scripting framework that can be used to deliver useful applications within the limited RAM and Flash memory resources of embedded processors such as the ESP8266.
Arduino IDE:
A core is the collection of software components required by the Board Manager and the Arduino IDE to compile an Arduino C/C++ source file down to the target MCU's machine language.
ESP8266 Arduino core comes with libraries to communicate over WiFi using TCP and UDP, set up HTTP, mDNS, SSDP, and DNS servers, do OTA updates, use a file system in flash memory, work with SD cards, servos, SPI and I2C peripherals.
It lets you write sketches using familiar Arduino functions and libraries, and run them directly on ESP8266

## Slide 6: ASM1117 (3.3V Voltage regulator)
The ESP-12E chip requires 3.3V power supply voltage.
NodeMCU ESP-12E dev board can be connected to 5V using micro USB connector or Vin pin available on board.
ESP-12E has a base voltage of 3.3V.
(Any voltages above 3.6 V may cause permanent damage to the chip. In case you have to interface with 5V I/O pins, you need to use level conversion system)

## Slide 7: Pin Definition of NodeMCU (LoLin)
Notes: Note: This info is related to ESP8266.
The ESP8266 has two hardware SPI modules. Espressif have named these SPI and HSPI.
SPI: This SPI module is capable of quad data channels and has 3x chip select pins available. However, it is already in use on 99.9% of modules where the operational code is loaded off a flash rom chip. It is incredibly difficult to use this for other devices at the same time without constant interruption. You can, however, mux the HSPI pins onto the same ones as the SPI module. The SPI module will take over control of the pins when it needs access (so you’re not guaranteed your HSPI operation all the time).
HSPI: Presumably this is meant to stand for HardwareSPI, but you can think of it as the User SPI. The pinout required is below.
Pin Name GPIO # HSPI Function
MTDI (HMISO) GPIO12 MISO (DIN)
MTCK (HMOSI) GPIO13 MOSI (DOUT)
MTMS (HSCLK) GPIO14 CLOCK
MTDO (HCS) GPIO15 CS / SS (Chip select/Slave select)
Pin Name is the one given in the datasheet. Note that the MTCK (which is a clock signal for something else) is NOT the clock for the HSPI! Same with the MTDO (data out) pin. It’s actually the HSPI Chip Select (or Slave Select). Easy to be confused.
Note: (NodeMCU takes care of this no need to worry while flashing )GPIO15 needs to be tied to GND when booting from the onboard SPI flash (see below table). Just use a suitable pull down resistor (4.7k or something) so the pin can still properly function as a chip select. Do not connect it directly to GND!
GPIO15 GPIO0 GPIO2 Mode Description
L L H UART Download code from UART
L H H Flash Boot from SPI Flash
H x x SDIO Boot from SD-card
SDIO: One Slave SDIO has been defined by ESP8266EX, 4bit 25MHz SDIO v1.1 and 4bit 50MHz SDIO v2.0 are supported.
RST: External reset signal (Low voltage level: Active).
GPIO16: For Deep sleep wakeup.

## Slide 8: Setting up Arduino IDE & NodeMCU
Open the Arduino IDE.
Go to Files and click on the Preference in the Arduino IDE.
Copy the URL below in the Additional boards Manager.
http://arduino.esp8266.com/stable/package_esp8266com_index.json
Click OK to close the preference Tab.

## Slide 9: ESP32
Open the Arduino IDE.
Go to Files and click on the Preference in the Arduino IDE.
Copy the URL below in the Additional boards Manager. https://dl.espressif.com/dl/package_esp32_index.json
Click OK to close the preference Tab.

## Slide 11
Go to Tools and Board, and then select Board Manager.

## Slide 12
Navigate to esp32 by Espressif Systems and install the software for Arduino.
Once all the above process has been completed we are ready to program our ESP32 with Arduino IDE.

## Slide 13
Connect NodeMCU to PC with USB to microUSB cable .
Windows should automatically download necessary drivers for it.

## Slide 14: Basics of Wi-Fi
Devices that connect to Wi-Fi network are called stations.
Connection to Wi-Fi is provided by an access point, that acts as a hub for one or more stations.
Each access point is recognized by a SSID (Service Set IDentifier).
Clients can access services provided by servers in order to send, receive and process data.
Server provide functionality to other programs or devices, called clients.
We need to use ESP8266WiFi library to make Wi-Fi applications on NodeMCU.

## Slide 15: WiFi library for ESP8266
WiFi.begin(ssid, password, channel, bssid, connect)
Meaning of parameters is as follows:
ssid - a character string containing the SSID of Access Point we would like to connect to, may have up to 32 characters
password to the access point, a character string that should be minimum 8 characters long and not longer than 64 characters
channel of AP, if we like to operate using specific channel (optional)
bssid - mac address of AP (optional)
connect - a boolean parameter that if set to false, will instruct module just to save the other parameters without actually establishing connection to the access point
WiFi.localIP()
Notes: Note:
WiFi.waitForConnectResult()
Function returns one of the following connection statuses:
WL_CONNECTED after successful connection is established
WL_NO_SSID_AVAILin case configured SSID cannot be reached
WL_CONNECT_FAILED if password is incorrect
WL_IDLE_STATUS when Wi-Fi is in process of changing between statuses
WL_DISCONNECTED if module is not configured in station mode
In case the connection is lost, ESP8266 will automatically reconnect to the last used access point, once it is again available. The same happens on module reboot. This is possible since ESP is saving credentials to last used access point in flash (non-volatile) memory. Using the saved data ESP will also reconnect if sketch has been changed but code does not alter the Wi-Fi mode or credentials.
ESP8266 can provide similar functionality except it does not have interface to a wired network. Such mode of operation is called soft access point (soft-AP). The maximum number of stations connected to the soft-AP is five.
The soft-AP mode is often used and an intermediate step before connecting ESP to a Wi-Fi in a station mode. This is when SSID and password to such network is not known upfront. ESP first boots in soft-AP mode, so we can connect to it using a laptop or a mobile phone. Then we are able to provide credentials to the target network. Once done ESP is switched to the station mode and can connect to the target Wi-Fi.
Another handy application of soft-AP mode is to set up mesh networks. ESP can operate in both soft-AP and Station mode so it can act as a node of a mesh network.

## Slide 16: Station Mode
WiFi.status()
Function returns one of the following connection statuses:
WL_CONNECTED after successful connection is established
WL_NO_SSID_AVAILin case configured SSID cannot be reached
WL_CONNECT_FAILED if password is incorrect
WL_IDLE_STATUS when Wi-Fi is in process of changing between statuses
WL_DISCONNECTED if module is not configured in station mode
WiFi.isConnected()

## Slide 17: Soft Access Point Mode
WiFi.softAP(ssid, password, channel, hidden)
The first parameter of this function is required, remaining three are optional.
Meaning of parameters
channel - optional parameter to set Wi-Fi channel, from 1 -13. Default channel is 1.
hidden - optional parameter, if set to true will hide SSID
Function will return true or false depending on result of setting the soft-AP
WiFi.softAPgetStationNum()
The maximum number of stations that may be connected to ESP8266 soft-AP is five.

## Slide 18: Scanning
WiFi.scanNetworks()
WiFi.scanNetworks(async, show_hidden)
Both function parameters are of boolean type.
asysnc - if set to true then scanning will start in background and function will exit without waiting for result. To check for result use separate function.
show_hidden - set it to true to include in scan result networks with hidden SSID.
WiFi.scanComplete()
Notes: Note:
Scanning for networks takes hundreds of milliseconds to complete. This may be done in a single run when we are triggering scan process, waiting for completion, and providing result - all by a single function. Another option is to split this into steps, each done by a separate function. This way we can execute other tasks while scanning is in progress. This is called asynchronous scanning.
WiFi.getNetworkInfo(networkItem, &ssid, &encryptionType, &RSSI, *&BSSID, &channel, &isHidden)
The networkItem is a zero based index of network discovered during scan. All other input parameters are passed to function by reference. Therefore they will be updated with actual values retrieved for particular networkItem. The function itself returns boolean true or false to confirm if information retrieval was successful or not.

## Slide 19: Client Mode
Create a client object using
WiFiClient client;
Declare server address using
IPAddress server(74,125,115,105);
client.connect(server, 80)
client.stop()
client.available()
Returns the number of bytes available for reading
client.write(data)
Write data to the server the client is connected to
client.read()
Read the next byte received from the server the client is connected to (after the last call to read()).
Notes: #include <WiFi.h>
client.flush()
Discard any bytes that have been written to the client but not yet read.

## Slide 20: Server Mode
WiFiServer server(80);
Creates a server that listens for incoming connections on the specified port.
server.begin()
server.available()
Returns a Client object, if no Client has data available for reading, this object will return false.
server.write(data)
Write data to all the clients connected to a server (one byte at a time).
To read data from client use available to get client object and use client.read() to read data.
Notes: setNoDelay(nodelay)
With nodelay set to true, this function will to disable Nagle algorithm.
This algorithm is intended to reduce TCP/IP traffic of small packets sent over the network by combining a number of small outgoing messages, and sending them all at once. The downside of such approach is effectively delaying individual messages until a big enough packet is assembled.

## Slide 21: Basic Example

## Slide 22: Writing your first program (sketch)
The code always has at least 2 functions
  setup()
  loop()
The setup() function is called when a sketch starts. Use it to initialize variables, pin modes, start using libraries, etc.
The setup function will only run once, after each power up or reset.
After creating a setup() function, which initializes and sets the initial values, the loop() function does precisely what its name suggests, and loops consecutively.
Its very similar to C/C++.

## Slide 23: Client

## Slide 24: Server

## Slide 25: PART2
ESP32

## Slide 26: SDK installation
https://github.com/yeokm1/iot-esp32-mcu-workshop
Install Serial Virtual Com Port drivers for your operating system if needed
  https://www.silabs.com/products/development-tools/software/usb-to-uart-bridge-vcp-drivers
Install Arduino IDE:
  https://www.arduino.cc/en/main/software
Install ESP32 SDK addon to Arduino IDE
  Add the following path to Additional Boards URL configuration
  https://dl.espressif.com/dl/package_esp32_index.json

## Slide 27: Components Check
ESP32 breakout board
50cm micro-USB cable
Half-size breadboard
Bunch of wires
In ESD bag
  Red LED
  Push button
  330 ohm resistor
  10k ohm resistor
330 ohm resistor
10k ohm resistor

## Slide 28: Agenda
Basics of Wifi
  Setup ESP32 as a Station
  Setup ESP32 as a AP
Basics of electronics
  Serial - Setting up of software SDK and testing
  Blink - Connecting and blinking LED
  Button - Connecting button and try to detect press
  Debounce - Concept of input debouncing
The “Internet” portion of IoT
  Post - Posting Request to a server on button press
  Get - Repeatedly polling the server for on or off instruction

## Slide 29: ESP32 chip vs ESP32 module vs ESP32 breakout

## Slide 30: ESP32 Specs
Specs | Value
CPU | Xtensa dual/single-core 32-bit LX6 microcontroller, operating at 160/240 MHz
RAM | 520 KiB
Flash memory | 4 - 16 MiB
Network Connectivity | Wifi 802.11n 2.4Ghz + BT 4.2
Peripheral Interfaces | 3x UART, 2x SPI, 2x I2C, ADC, SD touch sensors, etc

## Slide 32: Why not single-board computers like Raspberry Pi?
Specs | Arduino-compatible ESP32 | Raspberry Pi 4 B
CPU type | Microcontroller | Microprocessor
Speed | Dual Core 160/240Mhz | Quad core 1.5 Ghz
RAM | 520KB | 1 - 4 GB
GPU/Display | None | VideoCore VI GPU, 4K
Disk | 4 MiB | Depends on microSD card
Other connectivity | Wifi 802.11n 2.4Ghz + BT 4.2 | USB, Ethernet, HDMI, audio, Wifi 2.4/5Ghz 802.11ac, BT 5.0
Operating System | None | Linux (usually Raspbian)
Real Time Operation | Better | Poorer
Typical Power consumption | 0.8W | 8W
Price (SGD) | $30 | $50 - $80

## Slide 33: Arduino SDK
Easy to use cross-platform IDE for microcontroller programming
Support for many microcontrollers
C/C++ language
Numerous libraries

## Slide 34: 01-Serial
Verify Arduino SDK installed correctly as in the parent README.md
How to flash an Arduino program?
Using the serial console and ESP32 log facility

## Slide 35
Magnifying glass opens serial console
Show Timestamps
Newline
115200 baud

## Slide 36: 02-Blinky
Connect an LED
Blink from the LED

## Slide 37: Half/Full Breadboard
Base Prototyping component
Continuous lines indicate those holes are connected together
Horizontal usually for power
Convention: Red for +, Black/Blue for -
Vertical for your components

## Slide 38: LED
“A light-emitting diode (LED) is a semiconductor light source that emits light when current flows through it. ”
Diode: Component allowing one-way current flow
Anode +: Longer leg
Cathode -: Shorter Leg

## Slide 39: Resistor
Resists the flow of current
Resistor Colour bands
4-band 330 ohm
  Orange, Orange, Brown, Gold
  3, 3, x10, 5% tolerance
4-band 10K ohm
  1, 0, x1000, 5% tolerance
  Blown, Black, Orange, Gold

## Slide 40: Connecting the LED setup
Unplug USB cable before working on electronics
Breadboard + ESP32 board (G32, GND) + 330 ohm resistor + LED + wires
Pinouts may differ slightly from diagram. Always check the pin labels!
GND
G32

## Slide 41: Program the board with 02-blinky.ino

## Slide 42: 03-button button setup
10k ohm resistor + button + wires -> G34
Actual breakout 3V3 pin position differs from picture
“Pull down” resistor setup
GND
3V3
G32
G34

## Slide 43: Pull down resistor for button
Resistor “pulls” IO34 to ground when button is released
Guarantees that IO34 pin goes to 0
GND
3V3
G32
G34

## Slide 44: Program the board with 03-button.ino
We want to toggle LED on each button press
Observe looping speed of button press detection is too fast to be useful

## Slide 45: 04-debounce
Process one input within an interval

## Slide 46: 05-wifi-post
Making a POST request to the server via a button press
Able to receive a POST request using a Go program
WIFI_SSID: iot-workshop
WIFI_PASS: esp32isgreat
HOST: …

## Slide 47: 06-wifi-get
Making a Get Request to a server to get instruction
Serve a GET request using a Go program
WIFI_SSID: iot-workshop
WIFI_PASS: esp32isgreat
HOST: …

## Slide 48: Useful websites
http://frightanic.com/iot/comparison-of-esp8266-nodemcu-development-boards/
https://www.gitbook.com/book/krzychb/esp8266wifi-library/details
https://github.com/esp8266/Arduino/blob/master/doc/reference.md
http://www.esp8266.com/wiki/doku.php
https://github.com/esp8266/Arduino/blob/master/doc/libraries.md
http://esp8266.github.io/Arduino/versions/2.0.0/doc/libraries.html

## Slide 49: Thank You